ENVOY:

Envoy is a new high performance open source edge and service proxy which aims to make the network transparent to applications. Envoy’s out of process architecture allows it to be used alongside any language or runtime. At its core, Envoy is an L4 proxy with a pluggable filter chain model. On top of the L4 proxy it also includes a parallel pluggable L7 filter chain. Envoy is most comparable to software load balancers such as NGINX and HAProxy.

The network should be transparent to applications. When network and application problems do occur it should be easy to determine the source of the problem.

HOW:

Envoy runs on every host and abstracts the network by providing common features (load balancing, circuit breaking, service discovery, etc.) in a platform-agnostic manner. When all service traffic in an infrastructure flows via an Envoy mesh, it becomes easy to visualize problem areas, tune overall performance, and add substrate features in a single place.

A single Envoy deployment can form a mesh between Java, C++, Go, PHP, Python, etc. It is becoming increasingly common for service oriented architectures to use multiple application frameworks and languages. Envoy transparently bridges the gap.

On the other hand, suppose if we want to proxy different URLs to different back ends? That’s not possible with the typical L3/4 proxy: higher-level application information isn’t accessible down at these layers. Envoy deals with the fact by operating at layers 3, 4, and 7 simultaneously. This is extremely powerful, and can be very performant.

Pluggable filter chain mechanism allows filters to be written to perform different L3/L4 proxy tasks and inserted into the main server. Filters have already been written to support various tasks such as raw TCP proxy, HTTP proxy, TLS client certificate authentication, etc.

FEATURES:

Upgradation: Envoy can be deployed and upgraded quickly across an entire infrastructure transparently eliminating the pain of complex library upgrades.

HTTP L7 filter architecture: HTTP filters can be plugged into the HTTP connection management subsystem that perform different tasks such as buffering, rate limiting, routing/forwarding, sniffing Amazon’s DynamoDB, etc.

HTTP L7 routing: Envoy is capable of routing and redirecting requests based on path, authority, content type, runtime values, etc. This functionality is most useful when using Envoy as a front/edge proxy.

GRPC support: GRPC is Open source remote procedure call system from Google that uses HTTP/2 as the underlying multiplexed transport. Envoy supports all of the HTTP/2 features required to be used as the routing and load balancing substrate for GRPC requests and responses. The two systems are very complementary.

MongoDB L7 support: MongoDB is a popular database used in modern web applications. Envoy supports L7 sniffing, statistics production, and logging for MongoDB connections. MongoDB lacks decent hooks for observability but Envoy produces are invaluable when running sharded MongoDB clusters in production.

DynamoDB L7 support: Envoy supports L7 sniffing and statistics production for DynamoDB connections.

Service discovery: Service discovery is a critical component of service oriented architectures. Envoy supports multiple service discovery methods including asynchronous DNS resolution and REST based lookup via a service discovery service.

Health checking: Envoy includes a health checking subsystem which can optionally perform active health checking of upstream service clusters. Envoy then uses the union of service discovery and health checking information to determine healthy load balancing targets.

Advanced load balancing: Envoy is able to implement advanced load balancing techniques in a single place and have them be accessible to any application. Currently Envoy includes support for automatic retries, circuit breaking, global rate limiting and request shadowing.

Front/edge proxy support: Although Envoy is primarily designed as a service to service communication system, there is benefit in using the same software at the edge (observability, management, identical service discovery and load balancing algorithms, etc.). Envoy includes enough features to make it usable as an edge proxy for most modern web application use cases.

Best in class observability: As stated above, the primary goal of Envoy is to make the network transparent. However, problems occur both at the network level and at the application level. Envoy includes robust statistics support for all subsystems. Envoy also supports distributed tracing via third party providers.

ENVOY MESH:

Most applications involve two layers of Envoys. All of the Envoys form a mesh, and share routing information amongst themselves. The service Envoys can do health monitoring mesh know to check if any service is down. Also, Envoy’s statistics gathering works best with the full mesh.

    • First, there’s an “edge Envoy” running all by itself somewhere. The job of the edge Envoy is to give the rest of the world a single point of ingress. Incoming connections from outside come here, and the edge Envoy decides where they go internally.

    • Second, each instance of a service has its own Envoy running alongside it, a separate process next to the service itself. These “service Envoys” keep an eye on their services, and remember what’s running and what’s not.

DEMO-1:

Below demo shows how to configure Envoy as a proxy, allowing to forward traffic to external websites.

Source content is available in https://gitlab.pramati.com/krishnakumars/envoy

The above folder contains envoy.yaml file where all our listener and cluster configurations for envoy proxy are made. The configurations are writted to redirect the traffic to google.com

Clone the above repository and navigate to the folder and run below docker command.

docker run --name=proxy -d -p 8091:10000 -v $(pwd)/envoy.yaml:/etc/envoy/envoy.yaml envoyproxy/envoy:latest

This will start a container with port 8091 and our envoy.yaml file mounted to docker container.

Next, hit localhost:8091 in the browser and we should see google’s website.

DEMO-2:

Below is a simple front proxy topology running, which will send traffic to two service backends. Clone the above repository and move into examples/front-proxy directory. This contains Dockerfiles, config files and a Docker Compose manifest for setting up a the topology.

https://github.com/envoyproxy/envoy

The services run a very simple Flask application, defined in service.py. An Envoy runs in the same container as a sidecar, configured with the service-envoy.yaml file. Finally, the Dockerfile-service creates a container that runs Envoy and the service on startup.
The front proxy is simpler. It runs Envoy, configured with the front-envoy.yaml file, and uses Dockerfile-frontenvoy as its container definition.
The docker-compose.yaml file provides a description of how to build, package, and run the front proxy and services together.
docker-compose up --build -d

This starts a single instance of the front proxy and two service instances, one configured as “service1” and the other as “service2”. Docker-compose ps now shows 3 containers.

--build is used to build containers before starting up
 -d is used to run them in detached mode.

SENDING TRAFFIC:

Docker Compose has mapped port 8000 on the front-proxy to the local network. Open the browser to http://localhost:8000/service/1, or run curl localhost:8000/service/1
http://localhost:8000/service/2 or run curl localhost:8000/service/2

We can validate each request, while sent to the front envoy, was correctly routed to the respective application.

LOAD BALANCING:

Now let us try scale up one of the services to test the load balancing capabilities of envoy.

docker-compose scale service1=3

Now if we send a request to service1 multiple times, the front envoy will load balance the requests by doing a round robin of the three service1 machines

CONFIGURATIONS:
front-envoy.yaml:

Below is the front-envoy.yaml which is used by front proxy, the file has 2 elements, static_resources and admin.

admin:
  access_log_path: "/dev/null"
  address:
    socket_address:
      address: 0.0.0.0
      port_value: 8001

The access_log_path field is set to /dev/null. In a testing or production environment, we can change this value to an appropriate destination. The address object tells Envoy to create an admin server listening on port 8001.

The static_resources block contains definitions for clusters and listeners. A cluster is a named group of hosts/ports, over which Envoy will load balance traffic, and listeners are named network locations that clients can connect.

Our front proxy has a single listener, configured to listen on port 80, with a filter chain that configures Envoy to manage HTTP traffic.

  listeners:
  - address:
      socket_address:
        address: 0.0.0.0
        port_value: 80
  filter_chains:
    - filters:
      - name: envoy.http_connection_manager
        config:
        codec_type: auto
        stat_prefix: ingress_http
        route_config:
        name: local_route

Within the configuration for our HTTP connection manager filter, there is a definition for a single virtual host, configured to accept traffic for all domains. Routes are configured here, mapping traffic for /service/1 and /service/2 to the appropriate clusters.

        virtual_hosts:
        - name: backend
        domains:
        - "*"
        routes:
        - match:
        prefix: "/service/1"
        route:
        cluster: service1
        - match:
        prefix: "/service/2"
        route:
        cluster: service2

Below are some of the static cluster definitions.

  clusters:
  - name: service1
    connect_timeout: 0.25s
    type: strict_dns
    lb_policy: round_robin
    http2_protocol_options: {}
    hosts:
    - socket_address:
        address: service1
        port_value: 80

  - name: service2
    connect_timeout: 0.25s
    type: strict_dns
    lb_policy: round_robin
    http2_protocol_options: {}
    hosts:
    - socket_address:
        address: service2
        port_value: 80

MODIFYING CONFIGURATIONS:

In Envoy, we can modify the config files, rebuild Docker images, and test the changes. Listener filters are Envoy’s way of attaching additional functionality to listeners. For instance, to add access logging to the HTTP filter, add the access_log object to the filter config.

    - filters:
      - name: envoy.http_connection_manager
        config:
        codec_type: auto
        stat_prefix: ingress_http
        access_log:
        - name: envoy.file_access_log
        config:
        path: "/var/log/access.log"

Destroy the Docker Compose stack with docker-compose down, then rebuild it with docker-compose up --build -d. Make a few requests to the services using curl, then log into a shell with docker-compose exec front-envoy /bin/bash. An access.log file should be in /var/log, showing the results of the changes made.

COMPARISON WITH OTHER PROXIES:

HAProxy:

One of the proxies used over a decade is reliable, fast and proven proxy. HAProxy was initially released in 2006, when the Internet operated very differently than today. The velocity of the HAProxy community didn’t seem to be very high. For example, v1.5 added SSL after four years. There was challenges of hitless reloads (being able to reload the configuration without restarting the proxy) which were not fully addressed until the end of 2017

NGINX:

NGINX is a high-performance web server that does support hitless reloads. NGINX was designed initially as a web server, and over time has evolved to support more traditional proxy use cases.NGINX open source has a number of limitations, including limited observability and health checks.